## Slide 1: Smoke & Gas Monitor
BIU RACING · HACKATHON PROJECT
An early-warning air sensor that senses smoke, shows how close the air is to toxic, and sounds the alarm
STM32 Nucleo-G491RE · MQ-2 sensor · 16×2 I2C LCD · PWM buzzer
BIU Racing
Air OK
Notes: Hi, we're from BIU Racing, and this is our hackathon project: a smoke and gas monitor. It is a working prototype built on an STM32 Nucleo board, an MQ-2 gas sensor, a 16x2 LCD and a buzzer. In the next few minutes: the problem, a live demo, how it works, and where we'd take it next.

## Slide 2: Smoke is easy to miss until it's serious
Hard to notice early
A small gas leak or the first wisp of smoke is easy to miss, especially in a busy room.
All-or-nothing alarms
A basic detector stays silent until it screams. You can't see the air getting worse.
Seconds matter
The earlier someone knows, the more options they have: ventilate, shut off the source, step out.
THE GOAL
A monitor that shows the air getting worse before it's dangerous, and can't be missed when it is.
Notes: The problem: a small gas leak or the first bit of smoke is easy to miss, especially when people are busy. And a basic detector is all-or-nothing: it's silent until it screams, so you never see the air getting worse. Early warning buys time to react. So our goal: a monitor that shows the air getting worse before it's dangerous, and can't be missed when it is.

## Slide 3: One small board that senses, shows and warns
Sense
An MQ-2 sensor reads smoke and combustible gas (LPG, propane, methane, hydrogen) four times a second.
Show
A 16×2 screen shows the air status and a live bar that fills as the air gets worse.
Warn
Two alarm levels, Air Toxic and Air Very Toxic: the buzzer beeps and the backlight flashes until the air clears.
Log
Every reading streams to a laptop over the same USB cable, for testing and tuning.
Notes: The solution is one small board that does four jobs. Sense: an MQ-2 gas sensor, sampled four times a second. Show: a 16x2 LCD with a live level bar. Warn: two alarm levels, Air Toxic and Air Very Toxic. Both beep the buzzer and flash the backlight until the air clears. Log: the same USB cable we program it with also streams every reading to a laptop, which makes testing and calibration easy.

## Slide 4: What you see
Power-up
BIU Racing
Warming up 10s
The sensor's heater settles for 10 s. Alarms are held off during the countdown.
Normal
BIU Racing
Air OK
The bar fills as the air gets worse. Empty = clean air.
Toxic
BIU Racing
Air Toxic
From 2.0 V: the buzzer beeps and the backlight flashes.
Very toxic
BIU Racing
Air Very Toxic
From 3.0 V: a full-width warning replaces the bar, with the same beep and flash.
Notes: This is what the LCD shows in each state. The text matches what the firmware actually prints. Power-up: the MQ-2 has a heater that needs time to settle, so for the first 10 seconds it shows a countdown and never alarms. Normal: 'Air OK' with a level bar. Empty means clean air; it fills as smoke or gas builds up. Toxic: from 2.0 volts the label changes to 'Air Toxic', and the buzzer and backlight flash together twice per second. Very toxic: from 3.0 volts the bar would be full anyway, so the whole line becomes 'Air Very Toxic', with the same beep and flash.

## Slide 5: Live demo
1
Power on
A short beep, then a 10 s warm-up countdown.
2
Clean air
“Air OK” with the bar near empty.
3
Add gas or smoke
The bar climbs. At 2.0 V: “Air Toxic”, beep and flash.
4
Add more
At 3.0 V: “Air Very Toxic” fills the whole line.
5
Clear the air
The alarm holds until the level drops below 1.8 V, then clears.
Laptop terminal · 115200 baud
BIU Racing smoke sensor started
Warming up, MQ2: 1480 mV, 49% of very toxic level
Air OK, MQ2: 712 mV, 23% of very toxic level
Air Toxic, MQ2: 2140 mV, 71% of very toxic level
Air Very Toxic, MQ2: 3060 mV, 100% of very toxic level
Air Toxic, MQ2: 1920 mV, 64% of very toxic level
Air OK, MQ2: 1750 mV, 58% of very toxic level
Example output. The format is exactly what the firmware prints.
Notes: Live demo. We power it on: a short beep, then a 10-second warm-up countdown. In clean air it shows Air OK with the bar near empty. Now we bring gas or smoke close to the sensor, for example gas from an unlit lighter. Watch the bar climb. At 2.0 volts it switches to Air Toxic, and the buzzer and backlight start flashing. At 3.0 volts the whole line becomes Air Very Toxic. When we take the gas away, notice it stays in alarm until the level drops below 1.8 volts: that's the hysteresis. The laptop shows every reading live, like the example on the right.

## Slide 6: How it works
MQ-2 sensor
smoke & gas, 5 V
Divider
10k + 20k
0–5 V
≤ 3.3 V
STM32G491
Nucleo-G491RE board
Cortex-M4 · 170 MHz
12-bit ADC reads the sensor
16×2 LCD
status + level bar
I2C · D14/D15
Buzzer
2.5 kHz alarm
PWM · D3
Laptop
live readings
USB · 115200 baud
Notes: Here is the whole system. The MQ-2 runs on 5 volts, so its analog output can go above what the STM32 can safely read. A 10k / 20k divider scales it down before it reaches pin A0. The STM32G491 on the Nucleo board reads it with its 12-bit ADC, decides the state, and drives three outputs: the LCD over I2C on D14/D15, the buzzer with a PWM signal on D3, and a laptop over the board's USB serial port.

## Slide 7: Two levels, no false alarms
3.0 V: Air Very Toxic
bar full
2.0 V: Air Toxic
alarm starts
1.8 V: alarm clears
must drop below this
Clean-air baseline
bar empty (calibrated)
1
10 s warm-up
Readings are ignored while the sensor's heater settles, so power-up never trips the alarm.
2
16-sample average
Each reading averages 16 ADC samples, smoothing out electrical noise.
3
Hysteresis
Trips at 2.0 V but only clears below 1.8 V, so it can't flicker at the edge.
4
Calibrated baseline
The bar's zero is set from a real clean-air reading, so the bar only rises when the air changes.
Notes: The gauge shows the two alarm levels: Air Toxic from 2.0 volts and Air Very Toxic from 3.0 volts, where the level bar is full. These are the default values; we'll tune them in testing. A smoke alarm that cries wolf gets ignored, so we also spent effort on avoiding false alarms. One: the first 10 seconds after power-up are ignored while the heater settles. Two: every reading is an average of 16 ADC samples. Three: hysteresis. It trips at 2.0 volts and only clears below 1.8 volts, so a reading hovering at the threshold can't make it flicker. Four: the bar's zero point comes from a real clean-air reading, so the bar only moves when the air actually changes.

## Slide 8: By the numbers
4 / s
sensor readings and screen updates every second
30 steps
on the level bar: 6 characters × 5 pixel columns
2.5 kHz
alarm tone, beeping twice a second with the backlight
34 KB
firmware size: under 7% of the 512 KB flash
Notes: A few numbers. It reads the sensor and refreshes the screen four times a second. The level bar has 30 steps, because we draw each of its 6 characters one pixel column at a time with custom LCD characters. The alarm tone is 2.5 kHz and beeps twice a second together with the backlight. And the whole firmware is about 34 KB, under 7% of the chip's flash, so there is a lot of room to add features.

## Slide 9: Clean, modular firmware
Application
main.c: read sensor, then update screen, alarm and log
Drivers
MQ2 · I2C_LCD · BUZZER
STM32 HAL
ADC · I2C · TIM (PWM) · UART
Hardware
Nucleo-G491RE + sensor, screen, buzzer
Swap a part, keep the rest
Sensor, screen and buzzer each have their own driver. Replacing one doesn't touch the others.
Tune it in one file
Alarm levels, warm-up time and the divider values all live in MQ2.h.
Builds with zero warnings
Standard STM32CubeIDE project on ST's HAL library.
Notes: The firmware is layered. The application logic in main.c only talks to three small drivers: MQ2 and BUZZER, which we wrote, and the open-source I2C_LCD driver from DeepBlueMbedded. Those sit on ST's HAL library. That means we can swap a part, for example a different sensor or a bigger screen, by changing one driver. All the tuning values live in one header file, MQ2.h, and the project builds with zero compiler warnings.

## Slide 10: Parts and wiring
Part | Connects to | Notes
STM32 Nucleo-G491RE | USB to a laptop | The brain. USB powers it and carries the log.
MQ-2 gas sensor module | AO → divider → A0 (PA0) | Runs on 5 V for its heater.
10 kΩ + 20 kΩ resistors | AO → 10 k → A0 → 20 k → GND | Keeps the ADC pin under 3.3 V.
16×2 LCD + I2C backpack | SDA → D14, SCL → D15 | I2C address 0x27; only 2 data wires.
Passive buzzer | S → D3 (PB3) | Driven by a PWM tone from timer TIM2.
All off-the-shelf parts, wired with jumper leads: no custom PCB needed for the prototype.
Notes: Everything is off-the-shelf. The Nucleo board, the MQ-2 module, a standard 16x2 LCD with an I2C backpack, a passive buzzer, and two resistors. The one wiring detail that matters: the MQ-2 output must go through the 10k / 20k divider, never straight into A0, because it can reach 5 volts.

## Slide 11: Where we are and what's next
DONE
Firmware ready
Sensing, level bar, two-level alarm and USB logging, all building cleanly.
NEXT
Bench test
Test with real smoke and gas. Set the clean-air baseline and both alarm levels.
THEN
Package it
A case and a USB power supply. Set the BOOT0 option so it starts on its own at power-up.
LATER
Grow it
Phone alerts through a Wi-Fi or Bluetooth add-on, a red/green status LED, more sensors.
Notes: Where we are: the firmware is done. Sensing, the level bar, the two-level alarm and the USB logging all work in code and build cleanly. Next is testing with real smoke and gas, which is also when we calibrate the clean-air baseline and both alarm levels. Then we package it: a case, a USB power supply, and one setting on the chip (the BOOT0 option byte) so it always boots straight into our program when powered on. Later ideas: phone alerts through a Wi-Fi or Bluetooth add-on module, a red/green status LED, and more sensors on the same board.

## Slide 12: Thank you
Smoke & Gas Monitor: sense it, show it, sound the alarm.
Ready to demo
Sensing, level bar, two-level alarm and live logging on one Nucleo board.
Early warning
Shows the air getting worse, not just when it's already too late.
Built to grow
Modular drivers and under 7% of the flash used: room for much more.
BIU Racing
Questions?
Notes: To sum up: it's ready to demo, with sensing, the level bar, the two-level alarm and live logging all on one Nucleo board. It gives early warning: you see the air getting worse, not just a beep when it's already too late. And it's built to grow: modular drivers and under 7% of the flash used. Thank you, happy to take questions.